## Slide 1
IBM HACKATHON 2026
GRIDPULSE
AI
Network-aware grid load optimisation & renewable performance advisor
A direct answer to the challenge: predict → recommend → detect → explain → validate → brief.
60-MINUTE LOOK-AHEAD
DEMAND
SOLAR + WIND
GRID RISK
ACTION
HUMAN-IN-THE-LOOP
No autonomous grid control
TEAM ANTIGRAVITY
DhruvKumar Mistry • Meet Patel • Kakkad Priyansh • Harsh Verma

## Slide 2
01 / THE CHALLENGE
Five operational questions. One integrated answer.
The challenge is not five separate ML features. It is a single decision workflow for grid operators.
GRIDPULSE AI | IBM HACKATHON
02
01
Forecast demand spikes
Can we see rising grid stress before it becomes difficult to manage?
02
Recommend load balancing
What constrained action should be considered?
03
Detect renewable anomalies
Which asset is performing abnormally?
04
Identify root cause
Why is that asset underperforming?
05
Generate operator brief
What should the operator know, validate and decide?

## Slide 3
02 / OUR ANSWER
GridPulse turns the challenge into one closed operational loop.
Every challenge requirement maps to a concrete pipeline capability and a visible operator outcome.
GRIDPULSE AI | IBM HACKATHON
03
FORECAST
Demand spike prediction
XGBoost demand model 60-minute future horizon
CHALLENGE COVERED
BALANCE
Load-balancing recommendation
Constrained linear optimization battery • DR • dispatch
CHALLENGE COVERED
DETECT
Renewable anomaly detection
Residual analysis + Isolation Forest asset-level health
CHALLENGE COVERED
EXPLAIN
Root-cause evidence
Peer deviation + telemetry signals ranked diagnostic candidates
CHALLENGE COVERED
BRIEF
Operator optimisation brief
Current state + future state + evidence + action + validation
CHALLENGE COVERED
Integrated output: a decision-ready operator brief — not five disconnected model screens.

## Slide 4
03 / HOW IT WORKS
Predictive intelligence sits upstream of the decision.
The architecture deliberately separates prediction, optimization, simulation and human approval.
GRIDPULSE AI | IBM HACKATHON
04
DATA
Grid telemetry • renewable assets • weather • resources • events
↓
PREDICT
Demand • solar • wind • demand-spike probability
↓
ASSESS
Grid risk • curtailment probability • asset anomalies • root cause
↓
RECOMMEND
Constrained optimization with resource limits
↓
VALIDATE
Baseline vs counterfactual future state
↓
DECIDE
Operator brief • GREEN / YELLOW / RED • human approval
Key principle: ML predicts. The optimizer computes. The simulator challenges. The operator decides.

## Slide 5
04 / FORECAST
1. Forecast demand spikes before the grid state arrives.
GridPulse forecasts the next 60 minutes and converts the result into an operational risk signal.
GRIDPULSE AI | IBM HACKATHON
05
DEMAND MAE
36.23 MW
vs 86.13 MW persistence baseline
DEMAND RMSE
52.02 MW
test set
DEMAND MAPE
1.64%
test set
SPIKE ROC-AUC
0.94
validation-tuned threshold
NOW
CURRENT STATE
2,655.7 MW demand
FORECAST
+60 MINUTES
2,667.0 MW predicted
Potential predictive warning horizon — forecasts remain subject to error.

## Slide 6
05 / BALANCE
2. Recommend load-balancing actions within hard limits.
GridPulse uses linear programming to turn future risk into bounded candidate actions — without autonomous execution.
GRIDPULSE AI | IBM HACKATHON
06
1
BATTERY
Charge / discharge
Power boundary
2
DEMAND RESPONSE
Reduce demand
Zone-specific limit
3
DISPATCH
Increase dispatch
Available capacity
4
CURTAILMENT
Explicit curtailment
Used only as a decision variable
WHY THIS MATTERS
The optimizer is a recommendation engine. It does not directly control the grid.
Solver: scipy.optimize.linprog / HiGHS • 5,552 timesteps solved • zero solver constraint violations

## Slide 7
06 / RENEWABLE HEALTH
3. Detect anomalies. 4. Explain why they happened.
Asset diagnostics combine expected-performance residuals, temporal degradation signals and Isolation Forest scoring.
GRIDPULSE AI | IBM HACKATHON
07
SOLAR 60M MAE
15.06 MW
~76.8% improvement vs baseline
WIND 60M MAE
6.98 MW
~62.7% improvement vs baseline
EVENTS DETECTED
2 / 3
validation events
CRITICAL ASSET
SOLAR_07
inverter failure signal
SOLAR_07
Observed ~50% expected output
Inverter failure
CRITICAL
SOLAR_03
Sustained underperformance
Soiling evidence
WATCH
WIND_04
Subtle sustained drift
Gearbox degradation signal
WATCH / MISSED

## Slide 8
07 / OPERATOR BRIEF
One brief that connects state, future, evidence and action.
The operator gets a decision-ready summary — without needing to inspect every underlying model.
INTEGRATED OPERATOR BRIEF
01
CURRENT STATE
Demand • renewable output • transmission • curtailment
02
FUTURE STATE
60-minute demand • generation • grid risk
03
EVIDENCE
Asset health • root cause • stress signals
04
RECOMMENDATION
Constrained load-balancing action
05
VALIDATION
Baseline vs counterfactual safety result
Traceable outputs • deterministic safety flags • authoritative numbers preserved
OPERATOR DECISION
GREEN
NORMAL OPERATION
Decision support only
HUMAN APPROVAL
REVIEW → APPROVE / HOLD
UNSAFE ACTION → RED
GRIDPULSE AI | IBM HACKATHON
08

## Slide 9
08 / DIFFERENTIATOR
We do not hide model failure. We operationalize it.
The counterfactual layer asks whether the proposed action actually improves the future state.
GRIDPULSE AI | IBM HACKATHON
09
BASELINE
~7,068.53 MWh
curtailment over evaluation rows
0 overload intervals
COUNTERFACTUAL OPTIMIZED
~100,488.57 MWh
simulated curtailment
23 overload intervals
⚠ ADVERSE COUNTERFACTUAL
Forecast error can make a reasonable-looking action unsafe.
This is why GridPulse requires validation + human approval instead of autonomous control.

## Slide 10
09 / DEMO STORY
Show the judges one story, not ten features.
The strongest demo follows the operational sequence from current state to safe decision.
GRIDPULSE AI | IBM HACKATHON
10
01
OBSERVE
Current demand, renewable output and transmission state
02
FORECAST
60-minute demand + solar/wind outlook
03
ASSESS
Grid risk + curtailment probability + asset health
04
RECOMMEND
Constrained load-balancing action
05
VALIDATE
Simulate the proposed action against the baseline
06
DECIDE
GREEN / YELLOW / RED operator brief
The final screen answers one question: “Is this action safe enough for a human to approve?”

## Slide 11
10 / IMPLEMENTATION
Built as a practical MVP — with the limits visible.
The implementation prioritizes an auditable decision path over unnecessary model complexity.
GRIDPULSE AI | IBM HACKATHON
11
TECH STACK
Python
Core pipeline
Pandas / NumPy
Data processing
Scikit-learn
Anomaly detection
XGBoost
Demand forecasting
SciPy / HiGHS
Optimization
Plotly + Streamlit
Operator dashboard
HONEST LIMITATIONS
• Continuous battery SoC cannot be verified without energy_capacity_mwh.
• Forecasts are predictive guidance and subject to error.
• Wind MAPE is unstable near zero generation.
• Root cause is evidence-based, not fully supervised.
• Simulation results are counterfactual estimates, not historical savings.
• No automatic grid-control execution.

## Slide 12
GRIDPULSE AI
Forecast the grid. Validate the action. Keep humans in control.
Directly addresses the challenge through one integrated operator workflow.
PREDICT
See demand & renewable conditions 60 minutes ahead
PROTECT
Test recommendations with counterfactual simulation
DECIDE
Deliver explainable risk flags with human approval
TEAM ANTIGRAVITY
DhruvKumar Mistry • Meet Patel • Kakkad Priyansh • Harsh Verma